## Slide 1
THEME 07 • BUILD YOUR OWN BOARDS
MICROBOARD
STUDIO
The bridge between Arduino code, MCU internals and the real board.
MICROBOARD // LIVE
USB CONNECTED
ATmega328P
MCU
D13
PB5
PORTB5
CODE → REGISTER → PIN → PHYSICAL OUTPUT
Interactive • Hardware-connected • Debuggable
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 2
THE PROBLEM
Arduino makes hardware accessible. Understanding it is still opaque.
Static pinouts show *where* a pin is. They rarely show what the MCU is actually doing.
02
01
Static pinout
Pin labels and alternate functions are listed, but the chain from Arduino API → MCU port/bit → register → physical output is hidden.
02
Debugging by trial & error
Students often discover pin conflicts, wrong modes and serial/hardware issues only after compiling, wiring and testing.
03
Simulation ≠ reality
A simulator can demonstrate logic, but the real board has actual pins, registers, serial state and physical outputs.
THE GAP
“I wrote the code. What exactly changed inside the MCU — and did the real board do it?”
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 3
THE SOLUTION
MicroBoard Studio
An interactive learning + configuration layer that connects software intent to real hardware state.
03
LEARN
Pin / peripheral
CONFIGURE
Modes & mappings
VISUALIZE
Code → registers
CONNECT
USB / serial
VERIFY
Physical state
LIVE EXAMPLE
pinMode(13, OUTPUT)
→
D13
→
PB5
→
DDRB bit 5 = 1
→ OUTPUT
The same mapping can be inspected, simulated and sent to the connected Arduino.
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 4
CORE EXPERIENCE
One board. Multiple views. One source of truth.
The current prototype is structured around the exact concepts in the project documentation.
04
PIN EXPLORER
D13 → PB5 PWM • SPI SCK • LED
PERIPHERAL MAPPER
UART • SPI • I²C PWM • ADC
CODE VISUALIZER
Arduino API → MCU hardware
REGISTER VIEWER
DDRx • PORTx • PINx bit-level state
HARDWARE MONITOR
Physical pin state via serial
LEARN MODE
Concepts + guided MCU understanding
KEY
The differentiator is the connection between these views and the physical board.
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 5
DIFFERENTIATOR
Not “another Arduino clone”
The custom-board direction becomes valuable because the software makes hardware state observable, understandable and safer.
05
CORE
01 LIVE HARDWARE LINK
The interface can connect to the real Arduino over serial and mirror supported pin states. The prototype firmware exposes SET / MODE / READ / STATUS commands.
CORE
02 CODE → MCU TRACE
Users can follow a command such as digitalWrite(13, HIGH) through D13 → PB5 → PORTB bit 5 → LED ON.
NEXT
03 CONFLICT-AWARE DESIGN
The planned platform can flag incompatible pin/peripheral assignments before they become wiring or runtime problems.
Why it matters:
the board becomes something the user can inspect, learn from and verify — not just program.
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 6
ARCHITECTURE
Hardware + software, designed as one system
Current implementation: React/Vite interface + Arduino firmware. The architecture is intentionally extensible to a custom board.
06
USER
Explore • code • inspect
MICROBOARD UI
React + TypeScript
SERIAL LAYER
Web Serial
BOARD
Arduino Uno / MCU
PIN DATA
Ports • bits • peripherals
VISUALIZATION
Board • registers • code
FIRMWARE
MODE • SET • READ • STATUS
EXTENSIBLE PATH
Arduino Uno prototype → custom MicroBoard PCB → ESP32 / STM32 / RP2040 support
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 7
DEMO FLOW
A 2-minute story judges can see
Show the physical board and the UI reacting together. Avoid a feature dump.
07
01
SELECT
Click D13
UI reveals PB5 / SPI SCK / LED
02
TRACE
Run code
pinMode + digitalWrite map to registers
03
CONNECT
Attach board
Serial handshake confirms hardware
04
ACT
Set HIGH
Physical LED changes + UI state updates
05
VERIFY
Read status
Board reports pin state back to UI
DEMO MESSAGE • “You can see what the code means — then see the real board do it.”
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 8
TECHNICAL DEPTH
The prototype is already a real software–firmware loop
The uploaded project contains a React interface and Arduino firmware implementing a serial command protocol.
08
FIRMWARE
STATUS
→ returns D0…D13 mode + level
MODE 13 OUTPUT
→ configures physical pin
SET 13 HIGH
→ drives D13 HIGH
READ 13
→ returns current state
FRONTEND
React 19 + TypeScript + Vite
UI
Pin Explorer • Code Visualizer • Register Viewer
HARDWARE
Arduino Uno / ATmega328P
LINK
Web Serial + firmware protocol
This is not a slideware-only concept: the project package includes build output and firmware.
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 9
MVP STATUS
What is real today vs. what comes next
Keeping this distinction explicit makes the submission more credible.
09
PROTOTYPE NOW
Interactive Arduino pin / peripheral views
Code-to-hardware visualization concepts
Register visualization components
Web Serial connection path
Arduino firmware: MODE / SET / READ / STATUS
Live physical pin-state handling for digital pins
NEXT HARDWARE ITERATION
Custom MicroBoard PCB / headers
Per-pin protection and sensing
Automatic pin planning
Conflict detection across peripherals
Signal / protocol visualization
Broader MCU support
Positioning:
Prototype = proof of interaction. Custom board = the product direction.
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 10
ROADMAP
From educational tool → hardware platform
Build depth in layers; each step reuses the same pin-mapping and hardware-connection foundation.
10
NOW
Uno + live digital I/O
PROOF
NEXT
Custom PCB + protection
BOARD
THEN
Conflict-aware planner
AUTOMATION
SCALE
ESP32 / STM32 / RP2040
PLATFORM
The same core loop remains:
MAP
VISUALIZE
CONNECT
VERIFY
→
real hardware feedback
MICROBOARD STUDIO • CURIOUSPARC 2026
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.

## Slide 11
CURIOUSPARC 2026 • THEME 07
MICROBOARD STUDIO
Make the invisible visible.
A hardware-aware development and learning platform that connects Arduino-level code to MCU internals and the physical board.
UNDERSTAND
See the path from pin to register.
CONNECT
Control and read the real board.
EXTEND
Evolve into a custom board platform.
THANK YOU
MicroBoard Studio | Theme 7
MICROBOARD STUDIO • BUILD YOUR OWN BOARDS
Basis: uploaded MicroBoard Studio project documentation + prototype code/firmware; hackathon context from CuriousPARC official site.